## Slide 1: DIGITAL COMMUNICATION III B.Tech-V SEM 20EC503

## Slide 2: UNIT-I PULSE MODULATION: Introduction,Sampling Process(ideal and flat top), Pulse-Amplitude Modulation, Pulse-Position Modulation, Quantization Process, Quantization Noise, Pulse Code Modulation: Encoding, Regeneration, Decoding, Delta Modulation, Differential Pulse Code Modulation, Line Codes.

## Slide 3
INTRODUCTION

## Slide 4
Source
It generates message to be transmitted. Examples are the data from computers, text data or tele type data. The source can be an analog signal. Example: A Sound signal
Input Transducer
This is a transducer which takes a physical input and converts it to an electrical signal (Example: microphone). This block also consists of an analog to digital converter where a digital signal is needed for further processes. A digital signal is generally represented by a binary sequence.
Source Encoder
The source encoder compresses the data into minimum number of bits. This process helps in effective utilization of the bandwidth. It removes the redundant bits unnecessary excess bits,i.e.,zeros

## Slide 5
Channel Encoder
The channel encoder, does the coding for error correction. During the transmission of the signal, due to the noise in the channel, the signal may get altered and hence to avoid this, the channel encoder adds some redundant bits to the transmitted data. These are the error correcting bits.
Digital Modulator
The signal to be transmitted is modulated here by a carrier. The signal is also converted to analog from the digital sequence, in order to make it travel through the channel or medium.
Channel
The channel or a medium, allows the analog signal to transmit from the transmitter end to the receiver end.

## Slide 6
Digital Demodulator
This is the first step at the receiver end. The received signal is demodulated as well as converted again from analog to digital. The signal gets reconstructed here.
Channel Decoder
The channel decoder, after detecting the sequence, does some error corrections. The distortions which might occur during the transmission, are corrected by adding some redundant bits. This addition of bits helps in the complete recovery of the original signal.
Source Decoder
The resultant signal is once again digitized by sampling and quantizing so that the pure digital output is obtained without the loss of information. The source decoder recreates the source output.
Output Transducer
This is the last block which converts the signal into the original physical form, which was at the input of the transmitter. It converts the electrical signal into physical output (Example: loud speaker).

## Slide 9
Sampling:-
Sampling is a process where an analog Signal is converted into a corresponding Sequence of Samples that are Usually spaced uniformly in time.
i.e. process of converting Continuous time Signal into discrete time Signal.
There are two types of Sampling :
1) Ideal Sampling or Impulse Sampling or Instantaneous Sampling
2) practical Sampling.
i) Natural Sampling & chopper Sampling
ii) Flat Top Sampling or Sample & Hold Sampling.

## Slide 10
The following figure indicates a continuous-time signal and a sampled signal . When is multiplied by a periodic impulse train, the sampled signal is obtained.

## Slide 11
Sampling frequency is the reciprocal of the sampling period. This sampling frequency, can be simply called as Sampling rate. The sampling rate denotes the number of samples taken per second, or for a finite set of values

## Slide 12
Nyquist Rate:
Suppose that a signal is band-limited with no frequency components higher than Hertz. That means, is the highest frequency. For such a signal, for effective reproduction of the original signal, the sampling rate should be twice the highest frequency.
Which means,
fs = 2W
Where,
fs is the sampling rate
W is the highest frequency
This rate of sampling is called as Nyquist rate.

## Slide 13
Statement:
A continuous time signal can be represented in its samples and can be recovered back when sampling frequency fs is greater than or equal to the twice the highest frequency component of message signal. i. e.
fs≥2fm
Proof:
Consider a continuous time signal x(t).
The spectrum of x(t) is a band limited to fm Hz i.e. the spectrum of x(t) is zero for |ω|>ωm.
Sampling of input signal x(t) can be obtained by multiplying x(t) with an impulse train δ(t) of period Ts.
The output of multiplier is a discrete signal called sampled signal which is represented with y(t) in the following diagrams:

## Slide 15
Here, you can observe that the sampled signal takes the period of impulse.
The process of sampling can be explained by the following mathematical expression:

## Slide 19: Sampling
Process of converting analog signal into discrete signal.
Sampling is common in all pulse modulation techniques .
The signal is sampled at regular intervals such that each sample is proportional to amplitude of signal at that instant.
Analog signal is sampled every s𝑒𝑐𝑠, called sampling interval.
is called sampling rate or sampling frequency.
𝑓𝑠=2𝑓𝑚 is Min. sampling rate called Nyquist rate.
Sampled spectrum (𝜔) is repeating periodically without overlapping.
Original spectrum is centered at 𝜔=0 and having bandwidth of 𝜔𝑚.
Spectrum can be recovered by passing through low pass filter with cut-off 𝜔𝑚.
For 𝑓𝑠 < 2𝑓𝑚 sampled spectrum will overlap and cannot be recovered back. This is called as Aliasing.

## Slide 20
Sampling can be performed with the help of sampler.
Sampling methods:
Ideal – An impulse at each sampling instant.
Natural – A pulse of Short width with varying amplitude.
Flat Top – Uses sample and hold, like natural but with single amplitude value.
Impulse sampling is not used for information exchange as it has very low power.
Flat top sampling is most widely used due to its noise mitigation capability

## Slide 21: Impulse Sampling
The instantaneous sampling results in the samples whose width approaches zero. Due to this, the power content in the instantaneously sampled pulse is negligible. Thus, this method is not suitable for transmission purpose.

## Slide 24: Flat Top Sampling or Rectangular Pulse Sampling

## Slide 25
Flat top sampling like natural sampling is also a practically possible sampling method. But natural sampling is little complex whereas flat top sampling is quite easy.
In flat-top sampling or rectangular pulse sampling, the top of the samples remains constant and is equal to the instantaneous value of the baseband signal x(t) at the start of sampling.
The duration or width of each sample is τ and sampling rate is equal to fs = 1 / Ts.
Figure shows the functional diagram of a sample and hold circuit which is used to generate the flat top samples.
Fig.:5(a) A sample and hold circuit to generate flat top samples (b) A general waveform of flat top sampling.
Fig. 5(b) shows the general waveform of flat top samples. From fig.5(b), it may be noted that only starting edge of the pulse represents instantaneous value of the baseband signal x(t).
Also the flat top pulse of g(t) is mathematically equivalent to the convolution of instantaneous sample and a pulse h(t) as depicted in fig.6.

## Slide 26
This means that the width of the pulse in g(t) is determined by the width of h(t) and the sampling instant is determined by delta function.
In fig. 5(b), the starting edge of the pulse represents the point where baseband signal is sampled and width is determined by function h(t). Therefore, g(t) will be expressed as,
Figure 6:Convolution of any function with delta function is equal to that function
Now, from the property of delta function, we know that for any function f(t)

## Slide 27
This property is used to obtain flat top samples.
It may be noted that to obtain flat top sampling, we are not applying the above equation directly here i.e., we are applying a modified form of the above equation.
Thus, in this modified equation, we are taking s(t) in place of delta function δ(t).
Observe that δ(t) is a constant amplitude delta function whereas s(t) is a varying amplitude train of impulses. This means that we are taking s(t) which is an instantaneously sampled signal and this is convolved with function h(t).
Therefore, on convolution of s(t) and h(t), we get a pulse whose duration is equal to h(t) only but amplitude is defined by s(t).
Now, we know that the train of impulses may be represented mathematically as,

## Slide 30
7

## Slide 31
Fig.8 : (a) Baseband signal x(t), (b) Instantaneously sample signal s(t), (c) Constant pulse width function h(t), (d) Flat top sampled signal g(t) obtained through convolution of h(t) and s(t)

## Slide 32: PAM GENERATION
In pulse-amplitude modulation (PAM), the amplitudes of regularly spaced pulses are varied in proportion to the corresponding sample values of a continuous message signal ( i.e the message signal is multiplied by a periodic train of pulses)
The pulses can be of rectangular form or some other appropriate shape.
The waveform of a PAM signal is illustrated in Figure.
There are two operations involved in the generation of the PAM signal:
Instantaneous sampling of the message signal m(t) every Ts seconds, where the sampling rate fs=1/Ts is chosen in accordance with the sampling theorem.
Lengthening the duration of each sample, so that it occupies some finite value T.

## Slide 33
The LPF at the beginning is placed in order to avoid aliasing of the samples.
The LPF passes only the low-frequency component of the signal and eliminates the high-frequency signal component.
The output of LPF is then provided to a modulator, where it gets mixed with the rectangular pulse train.
Basically, the pulsed carrier gets modulated by the message signal here. The rectangular carrier pulse is generated by the pulse generator circuit.
The modulator generates a pulse amplitude modulated signal.

## Slide 34
The sampled pulses can be achieved either by natural or flat top sampling.
The output of the modulator is provided to the pulse reshaping circuit which basically shapes the pulses so that it can be easily detected at the receiver.

## Slide 35: Aperture Effect:
This equation shows that the signal g(t) is obtained by passing the signal s(t) through a filter having transfer function H(f).
The corresponding impulse response h(t) in time-domain has been shown in fig.7 (a)
Each sample of x(t) [i.e., s(t)] is convolved with this pulse.
Equation (1) represents that the spectrum of this rectangular pulse is multiplied with that of s(t).
Fig.7(b) shows the spectrum of one rectangular pulse of h(t).
We know that the spectrum of a rectangular pulse is expressed as
(1)
(2)

## Slide 36
Hence, from fig.7(b), it may be observed that by using flat top samples an amplitude distortion is introduced in the reconstructed signal x(t) from g(t).
In fact, the high frequency roll-off of H(f) acts like a low-pass filter and thus attenuates the upper portion of message signal spectrum.
These high frequencies of x(t) are affected. This type of effect is known as aperture effect.
Now, as the duration ‘τ’ of the pulse increases, the aperture effect is more prominent. Hence, during reconstruction an equalizer is needed to compensate for this effect.
As shown in figure, the receiver contains a low-pass reconstruction filter with cutoff frequency slightly higher than the maximum frequency present in the message signal. The equalizer compensates for the aperture effect. It also compensates for the attenuation by a low-pass reconstruction filter.
Figure: Recovering the message signal m(t) from the PAM signal s(t)
(LPF) filter
X(f).H(f)

## Slide 37
From equation (2), it may be noted that the sample function h(t) acts like a low-pass filter where Fourier transform is expressed as,
Equalizer used in cascade with the reconstruction filter has the effect of decreasing the in band loss of the reconstruction filter as the frequency increases in such a way as to compensate for the aperture effect.
Also, the transfer function of the equalizer is expressed as,
Here ‘td’ is known as the delay introduced by low-pass filter which is equal to τ/2. Therefore
which is the transfer function of an equalizer.

## Slide 38
NOTE: The amount of equalization needed in practice is usually small.
Indeed, for a duty cycle T/Ts  0.1,The amplitude distortion is less than 0.5 percent, in which case the need for equalization may be omitted altogether.
Transmission Bandwidth in PAM
In a pulse amplitude modulated (PAM) signal the pulse duration ‘τ’ is considered to be very small in comparison to time period (i.e., sampling period) Ts between any two samples i.e.,
(1)
Now, if the maximum frequency in the modulating signal x(t) is fm, then according to sampling theorem, the sampling frequency fs must be equal to or higher than the Nyquist rate, i.e.

## Slide 41
ADVANTAGES:
It is a simple process for both modulation and demodulation.
Transmitter and receiver circuits are simple and easy to construct.
PAM can generate other pulse modulation signals and can carry the message at the same time.
The data can be transmitted quickly, efficiently, and effectively through usual copper wires in high volume.
DISADVANTAGES:
Bandwidth should be large for transmission PAM modulation.
Noise will be great.
Pulse amplitude signal varies so the power required for transmission will be more.
For transmitting PAM signal, BW must be large.

## Slide 42
Applications of PAM
It is used in Ethernet communication.
It is used in many micro-controllers for generating control signals.
It is used in Photo-biology.
It is used as an electronic driver for LED lighting.

## Slide 43: PULSE-WIDTH MODULATION (PWM)
In pulse-duration modulation (PDM),the samples of the message signal are used to vary the duration of the individual pulses. This form of modulation is also referred to as pulse-width modulation or pulse-length modulation.

## Slide 44: Pulse Position Modulation (PPM)
In PPM, the amplitude and width of the pulses is kept constant but the position of each pulse is varied in accordance with the amplitudes of the sampled values of the modulating signal.
The position of the pulses is changed with respect to the position of reference pulses.
The PPM pulses can be derived from the PWM pulses as shown in fig.1. Here, it may be noted that with increase in the modulating voltage the PPM pulses shift further with respect to reference.

## Slide 45
The vertical dotted lines drawn in fig.1 are treated as reference lines to measure the shift in position of PPM pulses.
The PPM pulses marked 1, 2 and 3 in fig.1 go away from their respective reference lines. This is corresponding to increase in the modulating signal amplitude.
Then, as the modulating voltage decreases, the PPM pulses 4, 5, 6, 7 come progressively closer to their respective reference lines.
Fig.1 : PPM pulses generated from PWM signal

## Slide 46: Generation of PPM Signal
The PPM signal can be generated from PWM signal as shown in fig.2 (a).
The PWM pulses obtained at the comparator output are applied to a monostable multivibrator. The monostable is negative edge triggered.
Hence, corresponding to each trailing edge of PWM signal, the monostable output goes high.
It remains high for a fixed time decided by its own RC components.
Thus, as the trailing edges of the PWM signal keep shifting in proportion with the modulating signal x(t), the PPM pulses also keep shifting, as shown in fig.3.

## Slide 48: Demodulation of PPM Signal
The PPM demodulator block diagram has been shown in fig.4 .
The operation of the demodulator circuit may be explained as under:
The noise corrupted PPM waveform is received by the PPM demodulator circuit.
The pulse generator develops a pulsed waveform at its output of fixed duration and applies these pulses to the reset pin (R) of a SR flip-flop.
A fixed period reference pulse is generated from the incoming PPM waveform and the SR flip-flop is set by the reference pulses.
Due to the set and reset signals applied to the flip-flop, we get a PWM signal at its output.
The PWM signal can be demodulated using the PWM demodulator.

## Slide 49
Advantages:
PPM has the most power efficiency as compared to other modulations.
This modulation has less stable amplitude noise interference.
This modulation separates the signal easily from a noisy signal.
It has constant transmitted power output.
It needs extremely less power as compared to PAM & PDM because of amplitude & short duration pulse.
Easy noise removal & separation is extremely easy in this type of modulation.
Power utilization is also extremely low as compared to other modulations because of stable pulse amplitude & width.
PPM communicates only simple commands from a Tx to an Rx, so it is frequently used in lightweight applications because of its low system necessities.

## Slide 50
Disadvantages
PPM is very complex.
It needs more bandwidth for transmission as compared to PAM.
It is extremely sensitive to multi-pathway interference like echoing that can disturb a transmission by changing the difference in arrival times of every signal.
Synchronization is necessary between transmitter & receiver which is not feasible each time & we require a dedicated channel for it.
Special devices are required for this kind of modulation.
Applications
The PPM is mainly used in telecommunication systems & air traffic control systems.
This modulation is used in radio control, an optical communication system & military applications.
This technique is used in planes, remote-controlled cars, trains, etc.
PPM is used in noncoherent detection wherever a receiver does not require any Phase lock loop or PLL to track the carrier’s phase.
It is used in RF (radio frequency) communication.
It is also utilized in high-frequency, contactless smart cards, radio frequency ID tags, etc.

## Slide 51: Difference Between PAM, PWM, and PPM

## Slide 54
In continuous-wave (CW) modulation, some parameter of a sinusoidal carrier wave is varied continuously in accordance with the message signal.
In pulse modulation, some parameter of a pulse train is varied in accordance with the message signal.
In this context, we may distinguish two families of pulse modulation, analog pulse modulation and digital pulse modulation, depending on how the modulation is performed.

## Slide 55
In analog pulse modulation, a periodic pulse train is used as the carrier wave, and some characteristic feature of each pulse (e.g., amplitude, duration, or position) is varied in a continuous manner in accordance with the corresponding sample value of the message signal.
Thus, in analog pulse modulation, information is transmitted basically in analog form, but the transmission takes place at discrete times.
In digital pulse modulation, on the other hand, the message signal is represented in a form that is discrete in both time and amplitude, thereby permitting its transmission in digital form as a sequence of coded pulses.

## Slide 64
Quantization:
The process of converting continuous amplitude levels into discrete amplitude levels is called as quantization
Quantization process:- The process of representing m(kTs) which is sampled value of m(t) at t=kTs is represented by finite set of representation levels.
Let m(t) is a analog input message signal m(kTs) represent the sampled amplitude of m(t) at t=kTs.

## Slide 67
For uniform Quantization Process
Where k= 1,2,3,…, L

## Slide 68
Total voltage range is divided into q equal intervals of step size S
where VH = Max. voltage value
VL = Min. voltage value
Draw mid lines representing quantization levels
Assign binary codes (pre-defined) to each quantization level
Calculate quantization error

## Slide 69
A 2-bit PCM modulator is used with a 0-1 V signal. What is the binary digital value that will occur for the following inputs: 0.4 V, 0.78 V. What is the quantization error for these two samples?

## Slide 73
Quantizing 0.4 V sample value: See that level 2 is near to 0.4 V. So, for sample voltage 0.4 V, 01 code is transmitted.
Quantization error e = 0.4 – 0.375 = 0.025 V
Quantizing 0.78 V sample: Level 4 is nearest to 0.78 V. So, digital code 11 is transmitted.
Quantization error e = 0.875 -0.78 = 0.095 V

## Slide 76
The major steps involved in PCM is
Sampling
Quantizing
Encoding
In pulse code modulation, the analog message signal is first sampled, and then the amplitude of the sample is approximated to the nearest set of quantization level.
This allows the representation of time and amplitude in a discrete manner. Thereby, generating a discrete signal.
This discrete signal is then converted into its binary form for the transmission of the signal.

## Slide 78
It is basically composed of a transmitter, a transmission path and a receiver.
The transmitter performs the sampling, quantizing and encoding of the signal.
The transmission path includes regenerative receivers that recover the signal from the undesired noise effects.
The receiver section that performs decoding of the coded signal after regeneration of the signal at the receiver

## Slide 81
The figure below shows the sampling of analog signal and further quantization of the samples

## Slide 90
Non-Uniform Quantization:
In non-uniform quantization, the step size is not fixed. It varies according to certain law or as per input signal amplitude.
The following fig shows the characteristics of Non uniform quantizer.

## Slide 93
Companding PCM System:
Non-uniform quantizers are difficult to make and expensive.
An alternative is to first pass the speech signal through nonlinearity before quantizing with a uniform quantizer.
The nonlinearity causes the signal amplitude to be compressed.
The input to the quantizer will have a more uniform distribution.
At the receiver, the signal is expanded by an inverse to the nonlinearity.
The process of compressing and expanding is called Companding.

## Slide 117
In Delta Modulation the step size is constant , so that its slope overload distortion and granular noise both can not be controlled.
This drawback is overcome by Adaptive delta modulation ,in which the step size is variable.

## Slide 120
Slope overload distortion will take place if slope of sine wave is greater than slope of delta modulator

## Slide 131
Differential pulse code modulation is a technique of analog to digital signal conversion. This technique samples the analog signal and then quantizes the difference between the sampled value and its predicted value, then encodes the signal to form a digital value.
Before going to discuss differential pulse code modulation, we have to know the demerits of PCM (Pulse Code Modulation).
The samples of a signal are highly correlated with each other. The signal’s value from the present sample to the next sample does not differ by a large amount.
The adjacent samples of the signal carry the same information with a small difference.
When these samples are encoded by the standard PCM system, the resulting encoded signal contains some redundant information bits. The below figure illustrates this.

## Slide 133
The above figure shows a continuing time signal x(t) denoted by a dotted line.
This signal is sampled by flat-top sampling at intervals Ts, 2Ts, 3Ts…nTs.
The sampling frequency is selected to be higher than the Nyquist rate.
These samples are encoded by using 3-bit (7 levels) PCM.
The samples are quantized to the nearest digital level as shown by small circles in the above figure.
The encoded binary value of each sample is written on the top of the samples.
Just observe the above figure at samples taken at 4Ts, 5Ts, and 6Ts are encoded to the same value of (110).
This information can be carried only by one sample value. But three samples are carrying the same information means redundant.

## Slide 134
Now let consider the samples at 9Ts and 10Ts, the difference between these samples only due to the last bit and first two bits are redundant since they do not change.
So in order to make the process this redundant information and to have a better output.
It is an intelligent decision to take a predicted sampled value, assumed from its previous output and summarize them with the quantized values.
Such a process is called a Differential PCM (DPCM) technique.

## Slide 162
PCM-Each and every sample is encoded and transmitted
DPCM-Difference between samples is encoded and transmitted..so that some band width is saved.
DM-Difference between samples is encoded to only one bit and transmitted..so that more band width is saved.
ADM-Variable step size