## Slide 1: OP-AMP APPLICATIONS
The summing amplifier, Differential and instrumentation amplifiers, Voltage to current and current to voltage conversion, The Op-amp with complex impedances, Differentiators and integrators.

## Slide 2: Summing amplifier (Adder)
One of the important application of an Operational Amplifier is the Summing Amplifier or otherwise known as Adder.
As the name suggests, a Summing Amplifier is an Op-amp based circuit where multiple input signals of different voltages are added.
Summing amplifiers are of 2 types.
1.Inverting summing amplifier
2. non-inverting summing amplifier

## Slide 3: Inverting summing amplifier
Many applications in electronic circuits requires two or more signals to be added or combined into a single output.
Summing amplifier is also called as Voltage adder since its output is the addition of voltages present at its input terminal.
Summing amplifier uses an inverting amplifier configuration, i.e. the input is applied to the inverting input terminal of the op-amp, while the non-inverting input terminal is connected to ground.
Due to this configuration, the output voltage is out of phase with respect to the input by 180o.

## Slide 4: Circuit of inverting summing amplifier

## Slide 5: Analysis of inverting summing amplifier
In the circuit, the input signals Va , Vb , Vc are applied to the inverting input of the op-amp through input resistors Ra , Rb , Rc .Any number of input signals can be applied to the inverting input in the above manner. Rf is the feedback resistor , RL is the load resistor.Non inverting input of the op-amp is grounded using Rm resistor. By applying kirchhoff’s current law at node V2 we get,
Ia + Ib + Ic = If + Ib
Since the input resistance of an ideal op-amp is close to infinity and has infinite gain. We can neglect Ib , no current flows into the op-amp. Therefore Ia + Ib + Ic = If ……….(1)
Now V1 is grounded , hence V2 is at virtual ground.
Hence V2 = 0
I

## Slide 6: Equation (1) can be rewritten as (Va - 0) /Ra + (Vb- 0)/Rb + (Vc- 0)/Rc = (0 - V0)/Rf we get (Va/Ra) + (Vb/Rb)+ (Vc/Rc) = -V0/Rf Vo = -Rf ((Va/Ra) + (Vb/Rb)+ (Vc/Rc)) Vo = - {(Rf/Ra )Va + (Rf/Rb) Vb + (Rf/Rc) Vc }……..(2) If resistor Ra, Rb, Rc has same value i.e. Ra=Rb=Rc=R, then equation (2) can be written as V0 = - (Rf/R) x (Va + Vb +Vc)…………….(3) If the values of Rf = R , then the o/p voltage becomes, V0 = - (Va + Vb + Vc)-----------------(4) This indicates that the output voltage is the sum of the input voltages and is inverted i.e. out of phase with the input signal.

## Slide 7: Voltage Adder Example

## Slide 8: The closed loop voltage gains of each channel can be calculated as shown below ACL1 = – (Rf / R1) = – (100kΩ / 20kΩ) => ACL1 = -5 ACL2 = – (Rf / R2) = – (100kΩ / 10kΩ) => ACL2 = -10 ACL3 = – (Rf / R3) = – (100kΩ / 50kΩ) => ACL3 = -2 The output voltage of the inverting summing amplifier is given as, VOUT = – (ACL1 V1 + ACL2 V2 + ACL3 V3) = – [(5x 100mV) + (10x200mV) + (2x300mV)] = – (0.5 V + 2 V + 0.6 V) VOUT = – 3.1 V

## Slide 9: Non-inverting summing amplifier

## Slide 10: Analysis of Non-inverting summing amplifier
Using super position theorem we can find the total output voltage, V0 = V0a + V0b + V0c
V0 = (1+ Rf /R1 ). {VaR/2 + VbR/2 + VcR/2 } / (R + R/2)
V0 = (1+ Rf /R1 ). (Va/3 + Vb/3 + Vc/3)
By selecting Rf =2R1
Then V0 = ( Va + Vb + Vc )
We can conclude that the output voltage is sum of the three input voltages without any polarity change or in phase with the input voltages.

## Slide 11: Differential amplifier (difference amplifier- subtractor) with one op-amp

## Slide 12: Analysis of differential amplifier
Using super position theorem we can find the total output voltage, V0 = V01 + V02
V0 = - (R3/ R1) x V1 + (1+ R3 /R1 ). V2 (R4 / R2 +R4 )
By selecting R1 =R2 = R3 =R4
Then V0 = V2 – V1
We can conclude that the output voltage is the difference of the input voltages.

## Slide 13: Instrumentation amplifier
1.In many industrial , biomedical and consumer applications the measurement and control of physical conditions are very important like temperature , humidity , light intensity , water flow , pressure , bio electric potentials ,etc.
2. All these are measured by transducers , sensors and be amplified to drive indicators , display devices or processors , etc.
3. So we require high gain , high input impedance , low output impedance , high CMRR ,high slew rate and low power consumption amplifiers.
4. Hence an instrumentation amplifier is designed to amplify weak signals , added with noise with low thermal and time drifts .
5. Basically, the Instrumentation Amplifiers like µA 725 , ICL 7605 ,
LH 0036 ,INA 101 , PGA 201 are used.

## Slide 14: Design of Instrumentation amplifier

## Slide 15: Analysis of Instrumentation amplifier
In the instrumentation amplifier circuit we can have two stages with three op-amps.
First two op-amps (A1 , A2 ) acts as buffer amplifiers to provide high input impedance.
The last op-amp(A3 ) acts as differential amplifier with some gain (R4 / R3 )
Let a current of “ I “ flows from Vb to Va

## Slide 16: In this circuit Vb = V2 and Va = V1 , (because of virtual short concept ) Then the current I = ( Vb - Va ) / R1 = ( V2 - V1 ) / R1 Let the output voltages of A2 as V02 and A1 as V01 Then V02 = V2 + IR2 = V2 + (( V2 - V1 ) / R1) x R2 V01 = V1 – IR2 = V1 - (( V2 - V1 ) / R1) x R2 Finally the o/p voltage Vout = (R4 / R3) (V02 – V01) = (R4 / R3) { V2 + (( V2 - V1 ) / R1) x R2 - [ V1 - (( V2 - V1 ) / R1) x R2 ]} Vout = ( V2 - V1 )x ( 1+ 2 R2 / R1 ) x(R4 /R3)

## Slide 17: Voltage to current converter

## Slide 18: V- I converter
It is also called transconductance amplifier.
An op-amp based voltage to current converter produces an output current when a voltage is applied to its non-inverting terminal.
an input voltage Vi is applied at the non-inverting input terminal of the op-amp. According to the virtual short concept, the voltage at the inverting input terminal of an op-amp will be equal to the voltage at its non-inverting input terminal . So, the voltage at the inverting input terminal Vf of the op-amp will be Vi

## Slide 19: Analysis of V- I converter
Applying KCL at inverting i/p terminal ,
Vin / R1 - I0 = 0
Vin / R1 = I0
Hence I0 α Vin
Applications :
1. Low voltage ac and dc voltmeters.
2.Diode match finders
3.LED’s and Zener diode testers.
Drawbacks :
If larger currents are required we can use a power op-amp or a low power op-amp with an output current booster.

## Slide 20: Current to voltage converter

## Slide 21: Analysis of I- V Converter
Let us consider an inverting amplifier.
The o/p voltage is given by
Vout = ( - RF/ R1 ) VIN
Then Vout = - RF ( VIN / R1 )
We may write iin = ( VIN / R1 )
Hence Vout = - RF iin
Therefore Vout α iin
i.e. o/p voltage is proportional to i/p current
so we may redraw the ckt in the next slide.

## Slide 22: Current to Voltage converter using op-amp

## Slide 23: Current to Voltage converter using op-amp
Applications :
1.To detect current from photodetectors ,
photomultipliers.
2. Digital to Analog converters.
Sensitivity = Af = voltage gain
= change in o/p voltage/ change in i/p current
= ΔV0 / ΔIin
= - Rf
Drawback :
It has low sensitivity.

## Slide 24: Ideal Differentiator

## Slide 25: Analysis of differentiator
The basic op-amp differentiator circuit produces an output signal which is the first derivative of the input signal.
Applying KCL at node X ,
Iin = IB + If , but IB is very small ,
Hence Iin = If
But Iin = C { d/dt (Vin – 0 )} and If = (0 - Vout )/ Rf
Therefore C d/dt (Vin – 0 ) = (0 - Vout )/ Rf
C d (Vin ) /dt = - Vout / Rf
Vout = - CRf d (Vin) /dt
i.e. the output voltage is the differentiation of the input voltage

## Slide 26
The voltage gain of differentiator circuit is
Av = - Zf / Z1 = - Rf / ( 1 / jωC1)
= - jωRfC1 = I ωRf C1 I
Drawbacks :
1.When the voltage gain is unity, Av = 1
I ωRf C1 I = 1
Then the differentiator becomes unstable and break into oscillations.
2.Even the input impedance (Z1 = 1/jωC1) decreases with the increase of input signal frequency.
3.This makes the the circuit sensitive to high frequency noise. So the ideal differentiator is not suitable to practical applications, hence we have to consider practical differentiator.

## Slide 27: Practical differentiator

## Slide 28: Analysis of Practical differentiator
Voltage gain = Av = V0 / Vi = - Zf / Z1
= - ( Rf II CF ) / (R1 + JωC1 )
= - ( JωRFC1 )/ (1 + JωRFCF )(1 + jωR1C1 )
When RfCf = R1C1
Av = - jωRfC1 / (1 + jωR1C1 )2
I AV I = ω RfC1 /(1+ ω2R2C2)
For good differentiator the time period ( T ) of i/p signal ,
T ≥ RfC1
Advantage of practical Differentiator :
1. It is more stable.
2. it eliminates high frequency noise.

## Slide 29: Waveforms of Differentiator Circuit

## Slide 30: Ideal integrator

## Slide 31: Analysis of Ideal integrator
The op-amp based integrator produces an output voltage that is both proportional to the amplitude and duration of the input signal.
Applying KCL at node X ,
Iin = IB + If , but IB is very small ,
Hence Iin = If
Therefore (vI – 0 )/ R1 = C d/dt (0 – V0 )
dV0 /dt = - Vi / CRin
V0 = - ( 1/ CRin )ʃ Vi + k
Where k is integration constant
Finally Vo(s) = - (1/ sCRin) x Vi (s)
Voltage gain Av = V0(s) / Vi(s) = - (1 / sCRin ) = (1/ ωCRin )

## Slide 32
Drawback of Ideal integrator :
when frequency = 0 then , Av is very high .
hence the circuit will go into open-loop op-amp, and the output goes to saturation.
Applications :
1. Signal wave shaping circuits.
2. Analog to Digital converters.
3. Analog computers.

## Slide 33: Lossy or Practical integrator

## Slide 34: Analysis of practical integrator
Voltage gain (Av) = V0 / Vi
= - Zf / Zi
= - (R2II C) / R1
= - (R2 / R1) x { 1/ (1+ jωCR2)}

## Slide 35: Waveforms of Integrator Circuit