## Slide 1: CLIPPERS
Applications :These are wave shaping circuits used in digital computers , TV and FM receivers.
The clipper circuit consists of amplitude limiting element (Diode), Op-amp ,Resistors, RPS (to get the reference voltage )to clip some portion of input signals.
Clippers may be both positive and negative types.
The amplitude of input signal is always greater than the reference voltage

## Slide 2: 1.Positive Clipper

## Slide 3: Positive clipper Circuit operation
If positive parts of the input signal are clipped then it is called positive clipper.
The circuit acts as a voltage follower with a diode in the feedback path.
Clipping level is determined by reference voltage
The op-amp has to operate in closed loop and open loop simultaneously and must be high speed like HA2500 , LM310 , µA318 .
Positive clipper with positive Vref
when Vref =+1V
Case 1. When Vin > Vref
V01 is positive ,
Then the diode is OFF (Reverse Biased)
Now the output V0 = +Vref
Case 2. When Vin Vref,
V01 is negative
Then the diode is ON (Forward Biased)
Now the circuit acts as voltage follower. ( V0 = Vin )
The input and output waveform can be seen as shown below

## Slide 5
Positive clipper with negative Vref
When Vref = -1V
Case 1. When Vin > -Vref
V01 is positive ,
Then the diode is OFF (Reverse Biased)
Now the output V0 = -Vref
Case 2. When Vin < -Vref
V01 is negative
Then the diode is ON (Forward Biased)
Now the circuit acts as voltage follower. ( V0 = Vin )
The input and output waveforms can be shown below

## Slide 7: 2.Negative Clipper

## Slide 8
If negative parts of the input signal are clipped then it is called negative clipper.
The circuit acts as a voltage follower with a diode in the feedback path.
Clipping level is determined by reference voltage
Negative clipper with negative Vref
When Vref is negative ( Vref = -1V)
Case 1. If Vin > -Vref
Hence V01 is positive
Now diode is ON (Forward Biased)
So the circuit acts as voltage follower ( V0 = Vin )
Case 2. If Vin < - Vref
V01 is negative ,
Then the diode is OFF (Reverse Biased)
Now the output V0 = -Vref
The input and output waveforms are as follows

## Slide 10
Negative clipper with positive Vref
When Vref is positive ( Vref = +1V)
Case 1. If Vin > Vref
Hence V01 is positive
Now diode is ON (Forward Biased)
So the circuit acts as voltage follower ( V0 = Vin )
Case 2. If Vin < Vref
V01 is negative ,
Then the diode is OFF (Reverse Biased)
Now the output V0 = Vref
The input and output waveforms are as follows

## Slide 12: Clampers
A predetermined value of dc level is added to the output voltage .i.e. output is clamped to a desired dc level.
If clamped DC level is positive then the clamper is a positive clamper.
If clamped DC level is negative then the circuit is a negative clamper.
Output voltage of the clamper is a net result of ac and dc inputs applied to inverting and non inverting input terminals.
Vo = Vdc + Vac

## Slide 13: 1.Positive Clamper or Negative peak Clamper

## Slide 14
Case 1 : When DC Voltage i.e. when + Vref is applied to non inverting terminal
Diode is forward biased now the circuit acts as a Voltage follower.
Hence Vdc= + Vref
Case 2 : When AC Voltage is applied at inverting input terminal
During negative half cycle of Vi only the diode conducts.
Now the capacitor is allowed to charge through Diode to the negative peak value ( -Vm ).
During positive half cycle of Vi , Diode is reverse biased and the capacitor holds Vm .
So the the total output voltage Vo = Vdc + Vac
Vo = Vref + Vm + Vm
Vo = Vref + 2Vm

## Slide 15: The input and output waveforms of positive clamper

## Slide 16: 2.Negative Clamper or Positive peak clamper

## Slide 17
Case 1 : When DC Voltage i.e. when - Vref is applied to non inverting terminal
Diode is forward biased now the circuit acts as a Voltage follower.
Hence Vdc= - Vref
Case 2 : When AC Voltage is applied at inverting input terminal
During positive half cycle of Vi only the diode conducts.
Now the capacitor is allowed to charge through Diode to the negative peak value ( Vm ).
During negative half cycle of Vi , Diode is reverse biased and the capacitor holds Vm .
So the the total output voltage Vo = Vdc + Vac
Vo =- Vref - Vm -Vm
Vo = - (Vref + 2Vm )

## Slide 18: The input and output waveforms of negative clamper

## Slide 19
The value of capacitor depends on different input rates and pulse widths.
For precision clamping CRd << T/2
Where Rd = on resistance of diode, T= time period of input signal.
R =4.7kΩ is to protect op-amp from excessive discharge currents from capacitor when supplies are switched off

## Slide 20: Peak detector

## Slide 21
AC voltmeters are used to measure rms value of pure sinusoidal signals.
So it is not suitable to measure square , triangular , saw tooth waveforms (non-sinusoidal signals).
so peak values are measured for non sinusoidal signals using peak detector..
Let us consider a square wave as input.
Case 1: For positive half cycle of Vin D1 is forward biased, D2 reverse biased.
So the capacitor is allowed to charge to the positive peak value of Vin i.e. the circuit acts as a voltage follower
case 2: for Negative half cycle of Vin D1 is reverse biased and D2 forward biased.
Hence the capacitor will not be charging and retains the
voltage across it.

## Slide 22
For proper operation of circuit , charging and discharging constants must be CRd T/10 and CRL 10T
Where Rd on resistance of D1 , RL load resistance.
D2 helps to reduce recovery time of op-amp.
Negative peaks can be detected by reversing the diodes D1 ,D2
The input and output waveforms are shown below.

## Slide 23: Sample and Hold circuit

## Slide 24
Applications:
1. digital interfacing
2. communication systems (ADC , Pulse Modulations)
Circuit operation :
1. It samples an input signal and holds on to its last sampled value until the input is sampled again.
2. n-channel E-MOSFET acts as switch , controlled by the sample and hold voltage (Vs )
3. The capacitor serves as a storage element.
4. The analog signal which to be sampled is applied to Drain and control
voltage to Gate terminal of E-MOSFET.
5. For high positive value of Vs the Gate is closed and E-MOSFET
conducts. It allows the input voltage to charge the capacitor. Now
the voltage across capacitor will be the output voltage.
6. when control voltage Vs is low or negative , then the Gate is
opened and E-MOSFET is in OFF state ( nonconducting state) and
acts as a open switch.

## Slide 25
7.Now the capacitor does not charge and retains the last
sampled peak value till the next sampling period.
8. the voltage across capacitor appears at output of op-amp,
since it acts as a voltage follower.
9. During the switch is ON condition , the capacitor starts charging to the instantaneous value of i/p signal with a time constant
τ = (Ro + rds ON )C.
where Ro=output resistance of voltage follower (op-amp) ,
rds ON = is the ON resistance of E-MOSFET.
10. the frequency of control voltage should be kept high (twice) w.r.t. input signal frequency so as to retrieve the input from output waveform.
Sample and hold circuit available in IC form as LF398, LF198 ,HA2420. The input and output waveforms are shown below

## Slide 26
The time period (Ts ) of the control voltage Vs
during which the voltage across the capacitor is equal to the input voltage are called sample periods.
The time period (TH ) of the control voltage Vs
during which the voltage across the capacitor is constant are called hold periods

## Slide 27: Input and output waveforms of S/H circuit